## Slide 1: How CFD can improve the design process
CFD for Pump Design

## Slide 2: Agenda
What is CFD?
Why CFD?
Design Challenges
Test Case
  Pre-processing
  Simulation Set-up
  Post-processing
  Pump Curve
Result summary
Notes: Snap-shot is taken from the simulation of the test case pump in the following slides

## Slide 3: What is CFD?
Physical System
Mathematical Model
Discrete Model
Discrete Solution
Analytical modeling
Discretization
Solution
Describes the velocity and pressure fields in the computational domain
Gives the numerical solution of the Navier-Stokes equations
Notes: The area of interest is subdivided into a large number of cells. In each, the Navier-Stokes equations can be rewritten as algebraic equations that relate the velocity and pressure to the values in the neighboring cells
- Analytical modeling: formulation of the mathematical equations that models the physical problem (PDE + IC + BC)
- Discretization: reduction of the mathematical model to a discrete model
Solution: solution of the discrete problem on a digital computer.

## Slide 4: Why CFD?
Design
Test
Manufacture
Change design
Mass production
Design
Change design
CFD
Mass production
Without CFD
With CFD
Notes: - Better designs, lower risk, and faster time to the marketplace for the product

## Slide 5: Design Challenges
How to:
Choose the best blade count?
Choose the best blade angle?
Determine the optimum housing design?
Predict cavitation?
Determine pump curves?
Notes: To improve the accuracy of cavitation prediction:
  Proper boundary layer modeling
  Transient simulation
- Snap-shot is taken from the simulation of the test case pump in the following slides

## Slide 6: Test Case – Preprocessing
Mesh:
Elements: 6.4 million
Duration: 114 minutes
Core hours: 30.4
Rotating Zone:
Approach: Multi Reference Frame
Used for steady-state time dependency
Computationally cheaper than others
Notes: Steady-state is used for simulating constant flows

## Slide 7: Test Case – Simulation Set-up
Turbulence model:
K- SST
Predicts well at both, the wall and
away from it
Boundary conditions:
Velocity inlet (Flow rate = 2.61 )
Pressure outlet ( = 0 Pa)
No slip wall
Time dependency:
Steady-state
Notes: Since it is not possible to resolve the turbulence in small scales, turbulence models is used to reduce computation

## Slide 8: Test Case – Postprocessing
Velocity

## Slide 9: Test Case – Postprocessing
Pressure

## Slide 10: Test Case – Postprocessing
Streamlines

## Slide 11: Test Case – Postprocessing
Recirculation
Sharp corner can be removed to reduce recirculation

## Slide 12: Test Case – Postprocessing
Convergence
Notes: - Used to see how the model is converging through different iterations

## Slide 13: Test Case – Pump Curve
Data from the CFD results:
Inlet and outlet velocities
Inlet pressure
Equation:

## Slide 14: Test Case – Pump Curve
Data from the CFD results:
Moment (z-axis) of the impeller
z
Clockwise rotation
Equation:

## Slide 15: Test Case – Pump Curve
Best Efficiency Point
Equation:
Water power:

## Slide 16: Test Case
Area average
Volumetric flow rate | Mass flow rate | 
 | Inlet | Outlet
0.29 | 8.0E-05 | 8.0E-05
0.87 | 2.4E-04 | 2.4E-04
1.16 | 3.2E-04 | 3.2E-04
1.45 | 4.0E-04 | 4.0E-04
1.7 | 4.8E-04 | 4.8E-04
2.03 | 5.6E-04 | 5.6E-04
2.61 | 7.2E-04 | 7.2E-04
A stable and converged simulation:
Can be verified with an area average at the inlet and outlet
Notes: The mass flow rate is equal at the inlet and outlet

## Slide 17: Result Summary
CFD saves a lot of time and money
It can give pump curves
It is efficient for selecting the optimum:
  Blade number
  Blade angle
  Housing geometry
Notes: - Snap-shot is taken from the simulation of the test case pump in the following slides